Image Stream
Synchronization
for Visual Navigation
大矢グループ　i-ROBOT
Helio Perroni Filho

---
自律走行について「教示・再生」
- 例によるロボットに経路を教える
- プログラミングより簡単
- 訓練されているオペレータは要らない
出
先
出
発
点
オペレータ
「教示」ステップ
（経路で制御される）
1.
ロボット
「再生」ステップ
（自律走行）
2.
ロボット

---
自律走行について「教示・再生」
- 外観に基づいている自律走行
- カメラを使うのは色々な利点が有る：
  - ロバスト
  - コスト効率の良い
  - どこでも有る
  - 人間に直感的
目印
経路修正
「再生」ステップ
画像
（「教示」ステップ）
ドリフ
「教示」ステップ
画像
（「再生」ステップ）

---
自律走行について「教示・再生」
どのように「教示」の画像を「再生」の画像に合う?
「再生」ステップ
「教示」ステップ

---
自律走行について「教示・再生」
方法	参照	センサ	環境	変化
				照明	隠蔽面	動く物
テンプレト照合	[5]	単眼カメラ	室内	×	×	×
費用関数の最適化	[6]	単眼カメラ	室内	×	×	×
相互情報量	[7]	単眼カメラ	室内	×	○	○
特徴点の追跡	[8]	単眼カメラ	室内・室外	○	×	○
局所最大の相性	[9]	単眼カメラ	室外	○	○	○
ステレオ特徴点の相性	[10]	ステレオカメラ	室内	○	○	○
平均目印ベクトル	[11]	パノラマ式カメラ	室内	○	×	×
オプティカル・フロー	[12]	パノラマ式カメラ	室内	○	○	×
特徴点の相互相関		単眼カメラ	室内・室外	○	○	○
[Speaker Notes: Finding invariants that always apply can be tricky, though. Here I show some of the methods that have been proposed over the years – you can find the respective articles on my report's bibliography, these are their reference numbers. Most of these methods deal with computing a representation that is consistent across image variations, but fall short one way or another. A common limitation is for a method to only work indoors or outdoors. Difficulties on dealing with moving elements, such as people, or occlusions are also common. Some methods also require non-standard hardware, such as stereo cameras. Therefore, there is still demand for a teach-replay method that works well indoors and outdoors, uses simple hardware such as a single monocular camera, and can deal with changes in lighting and the presence of occlusion and moving objects.]

---
自律走行について「教示・再生」
- 自分の方法：「特徴点の相互相関」
- 特性
  - 画像シーケンスから安定な整合を作る
  - カメラ校正は要らない
  - 照明変化・隠蔽面・動く物にロバスト
  - 室内も室外も使えられる
[Speaker Notes: The limitations of current visual teach-replay methods have motivated me to look for a new solution, which I call Differential Visual Streams, or “DiVS” for short. It works on image sequences, generating stable representations that are robust to changes in lighting, occlusions and the presence of moving elements. It is applicable to indoors and outdoors environments, requiring a single, uncalibrated monocular camera as input. Last but not least, it is fast to compute, being convenient for real-time operation. Therefore, DiVS provides a sound base for the implementation of teach-replay on visual input.]

---
目次
- 自律走行について「教示・再生」
- 特徴点の相互相関
- 実験結果
- まとめ
[Speaker Notes: The DiVS method and its application to teach-replay are the subjects of the remainder of this presentation. In the next section I describe the DiVS method. Then I show how it can be used to implement a teach-replay control module for a mobile robot. Next I show the results of a number of experiments made with the control module, what conclusions can be drawn from those results, and discuss directions for further research.]

---
特徴点の相互相関
- 「再生」画像から特徴点を抽出する
- 各特徴点の近く広さαのパッチを抽出する
- 「教示」画像シーケンスの各画像から同じ特徴点の近く広さβのパッチを抽出する
- 各αパッチを同じ特徴点に関連してりるβパッチと相互相関して、最大出力のパッチを記録する

---
特徴点の相互相関
pi,kはp'j,kの
ベストマッチ
IiはI'jのベストマッチ
...
0
...
4
…
3
…
P
p'j,k
P(I'j) = [p'j,1, ..., p'j,z]
「再生」画像
I'j
pi,k
⭑
p'j,k
∑
Qi
ℙ
pi,k
ℙ(St) = [Q1, ..., Qm]
Qi = [pi,1, ..., pi,z]
「教示」画像シーケンス
St = [I1, ..., Im]
p'j,k
P(I'j)
P(I'j)
[Speaker Notes: Given a sequence of gray-scale images, the changes between successive images can be represented by the pixel-by-pixel absolute differences between them. The darker regions of such difference images show where the two images are very similar to each other, and the brighter regions, where they are different. This separation between “change” and “no change” regions can be enhanced by the application of a thresholding operation, such as Otsu's method. These thresholded difference images provide representations stable to lighting changes, but they are still affected by occlusions and moving elements. In order to account for that, we smooth out such transient changes by calculating the average over a sequence of difference images. These are what I call differential images, they show the amount of change in different regions of the visual field over a sequence window of some size w. Brighter pixels show high amounts of change, and darker ones, low amounts.]

---
特徴点の相互相関
...
0
...
2
…
3
…
...
0
...
4
…
3
…
...
4
...
2
…
0
…
...
...
「再生」画像のインデクス
I'j
P(I'1)
P(I'j)
P(I'n)
Ii
「教示」画像のインデクス
[Speaker Notes: Given a sequence of gray-scale images, the changes between successive images can be represented by the pixel-by-pixel absolute differences between them. The darker regions of such difference images show where the two images are very similar to each other, and the brighter regions, where they are different. This separation between “change” and “no change” regions can be enhanced by the application of a thresholding operation, such as Otsu's method. These thresholded difference images provide representations stable to lighting changes, but they are still affected by occlusions and moving elements. In order to account for that, we smooth out such transient changes by calculating the average over a sequence of difference images. These are what I call differential images, they show the amount of change in different regions of the visual field over a sequence window of some size w. Brighter pixels show high amounts of change, and darker ones, low amounts.]

---
目次
- 自律走行について「教示・再生」
- 特徴点の相互相関
- 実験結果
- まとめ
[Speaker Notes: The DiVS method and its application to teach-replay are the subjects of the remainder of this presentation. In the next section I describe the DiVS method. Then I show how it can be used to implement a teach-replay control module for a mobile robot. Next I show the results of a number of experiments made with the control module, what conclusions can be drawn from those results, and discuss directions for further research.]

---
実験結果
- システムパラメーター
  - 線速度 v = 0.3m/s
  - 画像サイズ640x320、入力周波数1Hz（毎秒1画像）
  - 画像シーケンス窓 w = 25
  - 方法パラメーター(α, β, z) = (30, 90, 10)
- 実験環境・経路
「室外」実験
「室内」実験
「教示」ステップ
2°
「再生」ステップ
「再生」ステップ
-2°
「教示」ステップ
20m
15m
[Speaker Notes: All field test procedures were performed under the same system parameters as shown here. During teach and replay steps I record odometry to provide an approximation for the robot's true location. Despite its limitations it is good enough for the scale of these tests. Teach step paths were just straight paths from the start point, with a length of 10 meters. Several teach paths were recorded. Starting from a common initial pose, the robot would make an initial in-place turn of up to 10°, and then set off in a straight line.]

---
実験結果
「室外」実験
教示
再生
「再生」画像のインデクス
もっと良い結果
画像シーケンスは完全一致
「教示」画像のインデクス
[Speaker Notes: Despite the differences in visual conditions and the presence of a moving element for much of the test record, the computed shifts for the 0° case either zero or negligible, correctly indicating the robot is treading much the same path as in the reference record. Results were very good for the 5° drift cases too: shift direction agrees with drift's, and numerical values are consistent. By the way, the time my implementation took to generate a single DiVS image on my lab notebook was 0.04 seconds on average.]

---
実験結果
「室内」実験
教示
再生
「再生」画像のインデクス
良い結果
画像シーケンスの不整合は低い
「教示」画像のインデクス
[Speaker Notes: Despite the differences in visual conditions and the presence of a moving element for much of the test record, the computed shifts for the 0° case either zero or negligible, correctly indicating the robot is treading much the same path as in the reference record. Results were very good for the 5° drift cases too: shift direction agrees with drift's, and numerical values are consistent. By the way, the time my implementation took to generate a single DiVS image on my lab notebook was 0.04 seconds on average.]

---
目次
- 自律走行について「教示・再生」
- 特徴点の相互相関
- 実験結果
- まとめ
[Speaker Notes: The DiVS method and its application to teach-replay are the subjects of the remainder of this presentation. In the next section I describe the DiVS method. Then I show how it can be used to implement a teach-replay control module for a mobile robot. Next I show the results of a number of experiments made with the control module, what conclusions can be drawn from those results, and discuss directions for further research.]

---
まとめ
- 特徴点の相互相関は画像シーケンスから整合を作る
- 整合は安定、環境の変化にロバスト
- 今後の予定
  - さらに実験
  - パフォーマンス向上
  - 他の線を整合する方法をやってみる（例：RANSAC）

---
終わり
以上
[Speaker Notes: This is the end of my presentation. Any questions?]